## Slide 1
Step 1 Tools required:
Small Phillips Screw Driver
Small Flathead or exacto razor
A Safe Open
1st use your thumb and index fingers to squeeze the middle of the ipod to create a small gap. Next insert the safe open tool and pry the front bezel along the full edge to open the unit.

## Slide 2: Step 2 You now have the front cover and backing apart. Be very careful because there are 2 ribbon cables still attached inside. One for the headphone jack and the other for the battery.

## Slide 3: Step 3 After the backing is pried up a little bit, take a small razor or flathead and pop the battery cable clip up to remove the Battery cable.

## Slide 4: Step 4 Picture of battery cable and how to remove.

## Slide 5: Step 5 Picture of battery cable removed.

## Slide 6
Step 6 Pull the hard drive out of the front panel and lay it down.

## Slide 7
Step 7 Next you are going to want to take the hard drive out. Gently pop the black clip up and remove the drive.